## Slide 1: Review of Results from the Electromagnetic Logging Network to Monitor Saltwater Movement on the Eastern Shore of Virginia
By Sam Caldwell
Hydrologist
USGS Virginia-West Virginia Water Science Center
This information is preliminary and is subject to revision. It is being provided to meet the need for timely best science. The information is provided on the condition that neither the U.S. Geological Survey nor the U.S. Government shall be held liable for any damages resulting from the authorized or unauthorized use of the information.

## Slide 2: Purpose and Scope of the Electromagnetic Logging Network
Is there saltwater movement occurring on the Eastern Shore of Virginia, and If so, where and how?
This question is addressed by:
Collecting discrete water levels and EM logs from 12 wells on the Eastern shore annually in August
Using those accumulated annual data to monitor for signs or evidence of saltwater movement on the Eastern Shore

## Slide 3: Eastern Shore Hydrogeologic Stratigraphy
Simplified stratigraphic relations among hydrogeologic units of the Eastern Shore. Figure from the Hydrogeologic Framework of the Eastern Shore (McFarland and Beach 2019)

## Slide 4
The State of Confined Groundwater Wells in the Eastern Shore
Figure of Eastern Shore water levels originally presented in 2017. Water levels is reported in feet above sea level
Water levels in the confined units of the Eastern Shore are mostly above sea level
There are three areas (shown in red) where confined water levels are at, or below sea level

## Slide 5: What is an Electromagnetic Induction (EM) Log?
A graph showing the bulk electrical conductance (mS/m) of the media surrounding a well
Logs can only be conducted on wells not cased with metal
Bulk resistivity is the combined resistivity of both the sediment around the well, and any water filling pores in the sediment
Sediment resistivity does not change year over year, so any change in a log is a result of change in the resistivity of the water in the pores between sediment
  This makes EM logs very useful in monitoring for saltwater movement over time
Logs are corrected for depth and conductance after collection for QA and QC before analysis

## Slide 6
Moving Average:
  Data smoothing technique used to identify trends and reduce noise caused by outliers
  This is achieved by using a moving average of the data
Chart: Smoothed data
Chart: Raw Data
Depth (ft)
Moving Average

## Slide 7: Reading an Electromagnetic Induction Log
Portions of a log with higher conductance (blue) generally correspond clay and silt deposits
  Indicative of a confining unit
Portions of a log with lower conductance (green) generally correspond with sand and gravel
  Indicative of an aquifer
Portions of a log where the conductance reading at the same depth is different from another year is indicative of a change in water chemistry (orange)
Chart: 63G 24 Conductance with Depth

## Slide 8: Groundwater Level
Discrete groundwater levels are collected at each site
Groundwater Levels are collected before each EM log is conducted
Levels are generally displayed in units of feet (ft) below land surface datum (BLSD)
Groundwater level data for all wells goes back several decades.
  Only data from 2008 (start of logging network) to present is used for analysis of EM logs
Many of these wells are not visited frequently: annually, or Bi-annually
  This limits the ability to observe trends in groundwater level over time, and how those trends influence results in EM logs
Land Surface
Water Table
Screened Interval
Depth BLSD
Measurement Point
Well

## Slide 9
The following slides summarize the borehole geophysical data collected for the Eastern shore.
Data are summarized for:
Areas with little change in aquifer conductance,
Areas varying local trends
Areas showing signs of potential saltwater intrusion.

## Slide 10
Areas With Little or No Change in Conductance
Areas with Varying Local Trends
Areas Showing Signs of Potential Saltwater Intrusion

## Slide 11
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
63F 16 shows slight increases in conductance from 2008 to 2020 (<5 mS/m)
Surficial Aquifer has seen the largest amount of change over the period of record
Changes in Surficial Aquifer from 2008 to 2016 may be due to drilling fluids working their way out of the bore hole
Cape Center
Location of
slide discussion
Chart: 63F 16 Conductance With Depth
UPCUDEP | 117 | 117
UPAQDEP | 142 | 142
MIDCUDEP | 193 | 193
MIDAQDEP | 236 | 236
Chart: 63F 16 Δ in Conductance Over Time
UPAQDEP | 142 | 142
MIDCUDEP | 193 | 193
MIDAQDEP | 236 | 236
UPCUDEP | 117 | 117

## Slide 12
Chart: 63F 16 Δ in Conductance Over Time
UPAQDEP | 142 | 142
MIDCUDEP | 193 | 193
MIDAQDEP | 236 | 236
UPCUDEP | 117 | 117
Seasonal variation in groundwater levels appears to be muted from late 2013 onwards. Small drop in 2020, will that be sustained?
  Results in a mean rise of water levels over time, however, does not exceed previous years’ peak levels
  2020’s water level does not show any response in log
No clear signs of saltwater intrusion
Cape Center continued
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Location of
slide discussion

## Slide 13
Chart: 63G 24 Δ in Conductance Over Time
UPCUDEP | 67 | 67
UPAQDEP | 129 | 129
MIDCUDEP | 166 | 166
MIDAQDEP | 180 | 180
LOCUDEP | 230 | 230
LOAQDEP | 260 | 260
Chart: 63G 24 Conductance with Depth
UPCUDEP | 67 | 67
UPAQDEP | 129 | 129
MIDCUDEP | 166 | 166
MIDAQDEP | 180 | 180
LOCUDEP | 230 | 230
LOAQDEP | 260 | 260
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Lower Confining Unit
Lower Aquifer
Saint Marys Confining Unit
Small increases in conductance down the log. Nearly no change in bottom half of log
Largest change in the surficial aquifers
  Possibly due to change in land use
Saint Marys Confining Unit sharply increases conductance with depth.
  Beginning of saltwater/freshwater interface?
  If so, no sign of change in depth of interface
Cheriton
Location of
slide discussion

## Slide 14
Chart: 63G 24 Δ in Conductance Over Time
UPCUDEP | 67 | 67
UPAQDEP | 129 | 129
MIDCUDEP | 166 | 166
MIDAQDEP | 180 | 180
LOCUDEP | 230 | 230
LOAQDEP | 260 | 260
Sparse water level data for 13-year period
  Data suggest that water levels are holding steady, or slightly increasing.
Cheriton continued
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Lower Confining Unit
Lower Aquifer
Saint Marys Confining Unit
Location of
slide discussion

## Slide 15
Chart: 63G 15 Δ in Conductance Over Time
UPCUDEP | 50 | 50
UPPCAQDEP | 114 | 114
UPAQDEP | 143 | 143
MIDCUDEP | 178 | 178
MIDAQDEP | 191 | 191
Chart: 63G 15 Conductance with Depth
UPCUDEP | 50 | 50
UPPCAQDEP | 114 | 114
UPAQDEP | 143 | 143
MIDCUDEP | 178 | 178
MIDAQDEP | 191 | 191
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Upper Paleochannel Aquifer
Almost no change to conductance down the log
Sharp change in top of Upper Confining Unit due to metal in the casing
Oyster
Location of
slide discussion

## Slide 16
Chart: 63G 15 Δ in Conductance Over Time
UPCUDEP | 50 | 50
UPPCAQDEP | 114 | 114
UPAQDEP | 143 | 143
MIDCUDEP | 178 | 178
MIDAQDEP | 191 | 191
Upper Paleochannel Aquifer
Excluding late 2015, water levels have stabilized since 2013. This is reflected in the stabilization of conductance in the middle confining layer
Slight upward trend in water levels during time of logging from 2016 to present. Dip in WL in 2020.
  No effect on base of log. Will this be sustained?
Oyster continued
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Location of
slide discussion

## Slide 17
Chart: 64J 11 Conductance with Depth
UPCUDEP | 46 | 46
UPAQDEP | 126 | 126
MIDCUDEP | 175 | 175
MIDAQDEP | 191 | 191
LOCUDEP | 224 | 224
LOAQDEP | 273 | 273
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Lower Confining Unit
Lower Aquifer
Slight increase in conductance from 2008 to 2020 in most of log. More pronounced in surficial aquifer
Largest change in surficial aquifer
  Possibly a result of a change in solute sources
Increasing salinity with depth in lower aquifer
  Beginning of saltwater/freshwater interface or increasing clay content?
Willis Wharf
Location of
slide discussion
Chart: 64J 11 Δ in Conductance Over Time
UPCUDEP | 46 | 46
UPAQDEP | 126 | 126
MIDCUDEP | 175 | 175
MIDAQDEP | 191 | 191
LOCUDEP | 224 | 224
LOAQDEP | 273 | 273

## Slide 18
Chart: 64J 11 Δ in Conductance Over Time
UPCUDEP | 46 | 46
UPAQDEP | 126 | 126
MIDCUDEP | 175 | 175
MIDAQDEP | 191 | 191
LOCUDEP | 224 | 224
LOAQDEP | 273 | 273
Groundwater level has been stabilizing since 2016
Small decrease in WL in 2020, Oct. WL shows recovery.
Willis Wharf continued
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Lower Confining Unit
Lower Aquifer
Location of
slide discussion

## Slide 19
Chart: 66K 2 Δ in Conductance Over Time
UPCUDEP | 28 | 28
UPAQDEP | 106 | 106
UPAQDEP | 202 | 202
MIDAQDEP | 212 | 212
LOCUDEP | 226 | 226
LOAQDEP | 241 | 241
Chart: 66K 2 Conductance with Depth
UPCUDEP | 28 | 28
UPAQDEP | 106 | 106
MIDCUDEP | 202 | 202
MIDAQDEP | 212 | 212
LOCUDEP | 226 | 226
LOAQDEP | 241 | 241
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Lower Confining Unit
Lower Aquifer
Near no net change in conductance
  Very small decrease in conductance from 2008 to 2020
Spikes in raw data correspond to metal in the well casing: screws, bolts
Baylys Neck
Location of
slide discussion

## Slide 20
Chart: 66K 2 Δ in Conductance Over Time
UPCUDEP | 28 | 28
UPAQDEP | 106 | 106
UPAQDEP | 202 | 202
MIDAQDEP | 212 | 212
LOCUDEP | 226 | 226
LOAQDEP | 241 | 241
Water levels are below sea level
Potential downward trend since 2017
  This has continued in 2020
Changes in water level do not appear to have an effect on conductance readings in the Lower Aquifer
Baylys Neck continued
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Lower Confining Unit
Lower Aquifer
Location of
slide discussion
Location of
slide discussion

## Slide 21
Areas With Little or No Change in Conductance
Areas with Varying Local Trends
Areas Showing Signs of Potential Saltwater Intrusion

## Slide 22
Chart: 64K 7 Conductance with Depth
UPCUDEP | 36 | 36
UPPCAQDEP | 60 | 60
PCCUDEP | 93 | 93
LOPCAQDEP | 110 | 110
MIDAQDEP | 133 | 133
LOCUDEP | 141 | 141
Surficial Aquifer
Upper Confining Unit
Paleochannel Confining Unit
Middle Aquifer
Lower Aquifer
Upper Paleochannel Aquifer
Lower Paleochannel Aquifer
Lower Confining Unit
Most of the log shows a small increase in conductance over the observation period.
Exception in the top of the surficial aquifer.
  consistent increases in conductance from year to year
Given the shallow location of the increase, saltwater intrusion is probably not the cause
Small, but persistent increase of conductance in Lower Aquifer
  Freshwater/saltwater interface?
Hacks Neck
Location of
slide discussion
Chart: 64K 7 Δ in Conductance Over Time
UPCUDEP | 36 | 36
UPPCAQDEP | 60 | 60
PCCUDEP | 93 | 93
LOPCAQDEP | 110 | 110
MIDAQDEP | 133 | 133
LOCUDEP | 141 | 141

## Slide 23
Chart: 64K 7 Δ in Conductance Over Time
UPCUDEP | 36 | 36
UPPCAQDEP | 60 | 60
PCCUDEP | 93 | 93
LOPCAQDEP | 110 | 110
MIDAQDEP | 133 | 133
LOCUDEP | 141 | 141
Water levels have increased over time and are above sea level.
  Reflected in homogeneity of the log from the Lower Paleochannel Aquifer to the Lower Aquifer.
  Possible decrease in water levels since 2016
Hacks Neck continued
Surficial Aquifer
Upper Confining Unit
Paleochannel Confining Unit
Middle Aquifer
Lower Aquifer
Upper Paleochannel Aquifer
Lower Paleochannel Aquifer
Lower Confining Unit
Location of
slide discussion

## Slide 24
Chart: 62G 15 Δ in Conductance (mS/m)
UP_CU_DEP | 64 | 64
UP_AQ_DEP | 100 | 100
MID_CU_DEP | 150 | 150
MID_AQ_DEP | 165 | 165
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Change in conductance did not change more that 10 mS/m from 2008 to 2020
Surficial and Middle Aquifers, Middle Confining Unit show small changes to conductance
Largest change is in surficial layer. Change in land use, precipitation around logging?
Middle Aquifer displays small increase in conductance from 2019 to 2020 (no more than 5 mS/m)
Bay Creek Resort
Location of
slide discussion
Chart: 62G 15 Δ in Conductance (mS/m)
UP_AQ_DEP | 100 | 100
MID_CU_DEP | 150 | 150
MID_AQ_DEP | 165 | 165
UP_CU_DEP | 64 | 64

## Slide 25
Chart: 62G 15 Δ in Conductance (mS/m)
UP_AQ_DEP | 100 | 100
MID_CU_DEP | 150 | 150
MID_AQ_DEP | 165 | 165
UP_CU_DEP | 64 | 64
Overall increase in water level over time. Sharp decrease in 2020. Will that be sustained? Possibly reflected in increase in conductance from 2019 to 2020 in the Middle Aquifer.
Surficial aquifer dynamics are likely a result of higher water levels and less seasonal variation in water levels
Oscillations in lower end of log need continued monitoring to tease out likely causes. Variable water level?
No clear signs of saltwater intrusion
Bay Creek Resort continued
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Location of
slide discussion

## Slide 26
Areas With Little or No Change in Conductance
Areas with Varying Local Trends
Areas Showing Signs of Potential Saltwater Intrusion

## Slide 27
Freshwater and Saltwater Dynamics
Just like an iceberg, much of the mass of water sits below sea level
When water levels drop, the base of the freshwater “bubble” rises as well
Conversely, when the water level rises, the base of the “bubble” sinks
Saltwater is more dense than fresh water
Due to this difference freshwater in the ground sits on top of the saltwater
  This happens in much the same way that an iceberg floats in the ocean
Sea Level
Sea Water
Fresh Water
Water Level

## Slide 28
Chart: 66M 18 Conductance with Depth
UPCUDEP | 37 | 37
UPPCAQDEP | 110 | 110
PCCUDEP | 138 | 138
MIDCUDEP | 151 | 151
MIDAQDEP | 166 | 166
LOCUDEP | 182 | 182
Surficial Aquifer
Upper Confining Unit
Paleochannel Confining Unit
Upper Paleochannel Aquifer
Middle Aquifer
Lower Confining Unit
Middle Confining Unit
Zero to small decreases in conductance down the log
conductance increase from 2008-2016 in surficial aquifer largely offset by decreases from 2016-2018
Lower aquifer shows consistent decreases in conductance likely due to an increasing water level
Small increase in conductance at base of log from 2019 to 2020
Withams
Lower Aquifer
Location of
slide discussion
Chart: 66M 18 Δ in Conductance Over Time
UPCUDEP | 37 | 37
UPPCAQDEP | 110 | 110
PCCUDEP | 138 | 138
MIDCUDEP | 151 | 151
MIDAQDEP | 166 | 166
LOCUDEP | 182 | 182

## Slide 29
Chart: 66M 18 Δ in Conductance Over Time
UPCUDEP | 37 | 37
UPPCAQDEP | 110 | 110
PCCUDEP | 138 | 138
MIDCUDEP | 151 | 151
MIDAQDEP | 166 | 166
LOCUDEP | 182 | 182
Water levels are mostly below sea level but increasing since about 2011.
Decrease in WL in 2020. Sustained? Potentially related to small increase in conductance at base of log from 2019 to 2020
Affects of this are seen in the base of the log in the consistent decrease in conductance
Withams continued
Surficial Aquifer
Upper Confining Unit
Paleochannel Confining Unit
Upper Paleochannel Aquifer
Middle Aquifer
Lower Confining Unit
Middle Confining Unit
Lower Aquifer
Location of
slide discussion

## Slide 30
Chart: 63J 3 Conductance with Depth
UPCUDEP | 56 | 56
UPPCAQDEP | 84 | 84
UPAQDEP | 92 | 92
MIDCUDEP | 132 | 132
MIDAQDEP | 171 | 171
LOCUDEP | 188 | 188
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Lower Confining Unit
Lower Aquifer
Paleochannel Aquifer
Saint Marys Confining Unit
Slight increase in conductance down log from 2008 to 2018
Major changes in St. Marys Confining Unit
  Decrease from 2008-2016
  Stabilized 2016-2018
  Small increase in conductance at base of log in 2020
Excellent example reflecting saltwater movement as a result of a rise in groundwater level.
Concord Wharf
Location of
slide discussion
Chart: 63J 3 Δ in Conductance Over Time
UPCUDEP | 56 | 56
UPPCAQDEP | 84 | 84
UPAQDEP | 92 | 92
MIDCUDEP | 132 | 132
MIDAQDEP | 171 | 171
LOCUDEP | 188 | 188

## Slide 31
Chart: 63J 3 Δ in Conductance Over Time
UPCUDEP | 56 | 56
UPPCAQDEP | 84 | 84
UPAQDEP | 92 | 92
MIDCUDEP | 132 | 132
MIDAQDEP | 171 | 171
LOCUDEP | 188 | 188
Shows a noticeable decrease in conductance from 2008- 2016
Lower water levels in 2008 than 2016 might explain this:
  Higher water levels means more fresh water pushing down on the saltwater interface
  Water levels largely stable during logging since 2016
Decrease in WL in 2020.
  Will this be sustained?
  Increase in conductance at base of log is possible a response to this decrease in WL
Concord Wharf continued
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Lower Confining Unit
Lower Aquifer
Paleochannel Aquifer
Saint Marys Confining Unit
Location of
slide discussion

## Slide 32
Chart: 65K 23 Conductance with Depth
UPCUDEP | 30 | 30
UPAQDEP | 81 | 81
MIDCUDEP | 161 | 161
MIDAQDEP | 172 | 172
LOCUDEP | 202 | 202
LOAQDEP | 217 | 217
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Lower Confining Unit
Lower Aquifer
Saint Marys Confining Unit
Increases in conductance corresponding to confining units
Two spikes in conductance in lower aquifer are probably due to metal in the well (possibly casing centralizers)
The steady increase in conductance in the Saint Marys Confining unit is possibly the beginning of the freshwater-saltwater interface or increasing clay content in the confining unit
Bayside
Location of
slide discussion
Chart: 65K 23 Δ in Conductance Over Time
UPAQDEP | 81 | 81
MIDCUDEP | 161 | 161
MIDAQDEP | 172 | 172
LOCUDEP | 202 | 202
LOAQDEP | 217 | 217
SMCUDEP | 248 | 248

## Slide 33
Chart: 65K 23 Δ in Conductance Over Time
UPAQDEP | 81 | 81
MIDCUDEP | 161 | 161
MIDAQDEP | 172 | 172
LOCUDEP | 202 | 202
LOAQDEP | 217 | 217
SMCUDEP | 248 | 248
UPCUDEP | 30 | 30
Groundwater is below sea level, but has been recovering since 2016. Sharp drop in WL in 2020, still above 2016 WL
Well is on the edge of a large cone of depression making continued monitoring of conductance in this well very important
Bayside continued
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Lower Confining Unit
Lower Aquifer
Saint Marys Confining Unit
Location of
slide discussion

## Slide 34
Chart: 66L 1 Conductance With Depth
UPCUDEP | 42 | 42
UPPCAQDEP | 111 | 111
PCCUDEP | 186 | 186
MIDAQDEP | 200 | 200
LOCUDEP | 229 | 229
LOAQDEP | 251 | 251
Chart: 66L 1 Δ in Conductance Over Time
UPCUDEP | 42 | 42
UPPCAQDEP | 111 | 111
PCCUDEP | 186 | 186
MIDAQDEP | 200 | 200
LOCUDEP | 229 | 229
LOAQDEP | 251 | 251
Surficial Aquifer
Upper Confining Unit
Paleochannel Confining Unit
Middle Aquifer
Lower Aquifer
Upper Paleochannel Aquifer
Lower Confining Unit
Slight increase in conductance from 2008 to 2018
Exception in the top section of the surface aquifer
Interference, probably from screws or other metal objects in the well casing, is present throughout the log
Not logged in 2020 due to equipment failure.
Chesser Road
Location of
slide discussion

## Slide 35
Chart: 66L 1 Δ in Conductance Over Time
UPCUDEP | 42 | 42
UPPCAQDEP | 111 | 111
PCCUDEP | 186 | 186
MIDAQDEP | 200 | 200
LOCUDEP | 229 | 229
LOAQDEP | 251 | 251
Water level is close to sea level and decreasing though 2015
Signs of increasing water lever from 2015-Present. Recorded water level above sea level during logging for the first time in history in 2020
Low water levels probably coincident with active pumping
Chesser Road continued
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Lower Confining Unit
Lower Aquifer
Saint Mary’s Confining Unit
Location of
slide discussion

## Slide 36
Chart: 67M 14 Conductance with Depth
UPCUDEP | 57 | 57
UPAQDEP | 124 | 124
MIDCUDEP | 188 | 188
MIDAQDEP | 220 | 220
LOCUDEP | 254 | 254
Chart: 67M 14 Δ in Conductance Over Time
UPCUDEP | 57 | 57
UPAQDEP | 124 | 124
MIDCUDEP | 188 | 188
MIDAQDEP | 220 | 220
LOCUDEP | 254 | 254
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Lower Confining Unit
Small increase in conductance throughout the log
Minimal change in lower confining unit since 2016
NASA WFF
Location of
slide discussion

## Slide 37
Sparse data, and frequent gaps make interpretation of water levels difficult
Water levels are below sea level and show no signs of recovery. This may be due to the well’s location within the cone of depression associated with the Chincoteague public supply wells
Potential for reversal of flow in the flow-system
Appears to be a sharp drop in water level from 2014 onwards
  This would help to explain the increasing conductance in the lower confining unit
NASA WFF continued
Surficial Aquifer
Upper Confining Unit
Middle Confining Unit
Upper Aquifer
Middle Aquifer
Lower Confining Unit
Location of
slide discussion
Chart: 67M 14 Δ in Conductance Over Time
UPCUDEP | 57 | 57
UPAQDEP | 124 | 124
MIDCUDEP | 188 | 188
MIDAQDEP | 220 | 220
LOCUDEP | 254 | 254

## Slide 38
Most of the Eastern Shore has water levels that are:
  above sea level
  Stable, or increasing through 2019
  Show no signs of saltwater movement, or potential signs of downward movement
  Many sites saw a decrease in WL in 2020 compared to the prior 3-4 years. This will be monitored to determine if these levels are outliers or the beginning of a new trend
Parts of the Northern Eastern Shore show:
  Water levels below sea level
  Potential signs of upward saltwater movement
Sparse or incomplete historic groundwater data limit ability to fully analyze EM Logs
Logging has not been going on long enough to establish a baseline for each well to normalize data from each year…but we are starting to get there
  Unable to log Chesser well due to major issue with logging equipment
Continued monitoring is necessary to confirm the possible signs of saltwater movement,
Continue monitoring for saltwater movement elsewhere
Conclusions

## Slide 39: Summary Table
Name | Local ID | Station ID | Depth | Unit in which Well is Screened | Log interpretations
WITHAMS | 66M 18 | 375723075344403 | 240 | Lower Aquifer | Small changes in conductance in the Surficial Aquifer from 2008 to 2016 have largely been nullified. Consistent decrease in conductance in Lower Aquifer since start of program, however a small increase in conductance occurred from 2019 to 2020. Water levels below sea level, but by less than 1ft and stable, and above '08 level. 2020 Water level is lowest recorded level since 2017 possibly reflected in the conductance increase in the base of the log from 2019 to 2020
NASA WFF | 67M 14 | 375617075273701 | 280 | Lower Confining Unit | No change through log. Increase in conductance from 2008 -2016. No changes since '16. Lowest water levels in network. Adjacent well in cluster (67M 13) shows signs of repeated pumping and is a good source for real-time water levels near this well. 2020 conductance shows near no change from 2019. 2020 water levels during logging are higher than the previous year's by over 5 ft.
CHESSER ROAD | 66L 1 | 375225075321701 | 305 | Lower Aquifer | No change in log since program started. However, well location between Chincoteague and poultry farm cones of depression necessitates further monitoring. Water level above sea level during logging for first time in program history. Not logged in 2020 due to equipment failure.
BAYSIDE | 65K 23 | 374442075432501 | 290 | St. Marys Confining Unit | No changes down length of the logs for the lifetime of the program. On SW edge of poultry farm cone of depression. Water levels below sea level, but less than 1ft, stable and recovering. Water levels still within 1ft below sea level, however 2020 water level is lowest since 2016 logging trip.
BAYLYS NECK | 66K 2 | 374320075380501 | 292 | Lower Aquifer | No changes in log since start of program. Water levels almost 3ft below sea level, but above 2008 level. Possible downward trend in water levels developing from 2016.
HACKS NECK | 64K 7 | 373845075522501 | 176 | Lower Aquifer | Most of the log shows no change. Small amount of change in last 10 ft of log, not showing much change. Consistent increases (though recently much smaller changes) in conductance in top 20 ft of log which are muted with depth but are present down to 50 ft. Suggests a surface derived source of conductance: possibly Fertilizer use change or flooding event from the Bay .Water levels above sea level and possibly trending down since 2016.
CONCORD WHARF | 63J 3 | 373230075541003 | 290 | St. Marys Confining Unit | No change in most of log, but there are consistent decreases in conductance in the last 30 ft of log, trend reversed from 2019 to 2020 with small increase in conductance at the base of the log. Large increase in water level from '08 to '16. Levels stable and trending slightly upward since 2016. Levels are below sea level. ~2ft drop in water level from 2019 to 2020, possibly reflected in increase in conductance at the base of the log.
WILLIS WHARF | 64J 11 | 373059075484503 | 313 | Lower Aquifer | Most of log shows no change in conductance. First 20 ft of log shows some yearly variations in conductance. Water levels are above sea level, trending upward, and appear to be stabilizing. Increase in conductance at the base of the log suggests the beginning of the freshwater-saltwater interface, which shows no movement for the life of the logging network.
CHERITON | 63G 24 | 371653075584803 | 330 | St. Marys Confining Unit | No change in log for lower 2/3 of log. Increase in conductance in top third of log from 2017 to 2018. Magnitude of change lessens to the base of the Upper Confining Unit and is not present in 2019 and 2020 logs. Water level was below sea level in 2008. Although water level data is sparse, levels have been above sea level and stable since 2016.
OYSTER | 63G 15 | 371709075560801 | 310 | Middle Aquifer | Near no change in the log. Small decrease in conductance in Middle Confining Unit from 2008 to 2016 likely drilling fluids working out of the bore hole. Water levels are above sea level and stabilizing.
BAY CREEK RESORT | 62G 15 | 371543076003401 | 190 | Middle Aquifer | Most of the logs show no change in conductance. The top 30 ft and last 10 ft of the log show small amounts of change from year to year. Cause is unknown. Water levels that were below sea level in 2008 are now above sea level and stabilizing. Water levels have been doing so since 2014. However, the 2020 water level was much lower and over 1ft below sea level (1929 NAVD)
CAPE CENTER | 63F 16 | 371307075583502 | 301 | Middle Aquifer | No change in log. Small decrease in conductance in middle of Surficial Aquifer from 2008-2016. Likely drilling fluids working out of the borehole. Water levels are above sea level and have been stable since 2016. This is reflected in the stability of the entire log since 2016.